## Slide 1: 5G-MOBIX GR-TR CBC Webinar
Vehicle development and Platooning UC
Tahir Sari (Platooning with See-What-I-See – FORD OTOSAN) GR-TR Webinar, June 29th, 2020

## Slide 2: Layout
Ford Truck Information
Platooning with See-What-I-See Application
  UC Overview, Diagrams
  TS-CBC collaboration with FI
  Early implementation video
Truck Routing in Customs Site
  UC Overview, Diagrams
Current GAPs from OEM Perspective
Project Overview & Key Achievements – 5GPPP TB eWorkshop – slide 2

## Slide 3: Ford Truck Information

## Slide 4: High Level Vehicle Architecture
International Truck of the Year 2019
Brake Module
Engine Control Module
Steering Module
Vehicle CAN
Control Block
Control ECU
Radar
Camera
4K Camera
«See-what-I-see»
LEVIS Client
OBU
microAutoBox dSpace
HMI
USB
Ethernet
Ethernet
Ethernet
Private CAN
Sensor
Prototype
Notes: OBU details will be explained by Kostas, at the next session.

## Slide 5: A bit detail…
Decision Maker
Platooning/Truck Routing State
Longitudinal Control
Lateral Control
ECM
Steering Control Unit
C-V2X
HMI
Vehicle speed, accelariton, platooning state&gap, GNSS information
Iniate‚Create platoon,
join request,
join accept,
join reject
Steering Decisions
Acc.
Decisions
What to do next
dSPACE MicroAutoBox
Sensors
Lane, Object
Info
Notes: OBU details will be explained by Kostas, at the next session.

## Slide 6: Platooning with See-What-I-See Application UC Overview & Scenarios

## Slide 7: Platooning with See-What-I-See Application
In a platoon, vehicles are moving much closer together than what would be possible if driven by human drivers
The reduced distance = greater fuel efficiency & reduced use of road space
Vehicles share their location, heading and speed as well as their intentions mainly over C-V2X Uu interface
PC5 interface as redundancy
Follower truck with autonomous acceleration/braking capabilities
4K video streaming from the leading truck to follower truck
Increased driver awareness & reduced anxiety levels

## Slide 8: Platooning with See-What-I-See Application
In your truck, you have a touchscreen in which you can search for nearby platoons.
If one is found, then you can send a “join” request.

## Slide 9: Platooning with See-What-I-See Application
The platoon leader will have to approve it. If he does, you can then approach the platoon
Location is displayed on the touchscreen and take the last place on the column.

## Slide 10: Platooning with See-What-I-See Application
At this point, the automatic system will take over and your vehicle will be automatically driven.
Once this integration is complete, you can request access from the leading driver to a "see what I see“ application.

## Slide 11: Platooning with See-What-I-See Application
Application allows you to see a continuous stream from a camera positioned on the leader’s windshield and pointed forward.
You can have a continuous vision of the road ahead of the leader and your cruise will be safer and more comfortable.

## Slide 12: Streaming Application
Video
stream
LEVIS Streaming
Servers
5G C-V2N
LAN Network (Ethernet connection)
LEVIS-Client
Jetson TX2
Video
stream
4K
Camera
5G C-V2N
HMI
OBU
OBU
LAN Network (Ethernet connection)
LEVIS-Client
Jetson TX2

## Slide 13: Vehicle Controller Early Implementations
https://www.youtube.com/watch?v=sirzW3AiPhU&t=31s

## Slide 14: Truck Routing in Customs Site Application UC Overview & Scenarios

## Slide 15: Truck Routing in Customs Site
TURKEY
GREECE
Core Network
Truck routing
  Sensor fusion technique for truck manoeuvres at the customs site
  Decreased average border crossing time
  Prevention of accidents
    5G Connected Truck Visit checkpoints autonomously
TURKEY
X-ray Building
CUSTOMS SITE
Plate
recognition
AI-based
X-ray data processing
TÜBİTAK BİLGEM
Electronic file storage system
Machine learning and deep learning
Integration into all customs gates
Store and make sense of X-ray scanning images of containers and trucks to cross the border
GREECE

## Slide 16: Scenario 2: Truck Routing in Customs Site
When you reach the border control facility you will see the message ‘Autonomous Truck Routing Application is available at this border’ written as road sign
After that point you can enable the ‘Autonomous Truck Routing Application’ via a tablet placed on your dashboard and the application will take over control of the truck.

## Slide 17: Scenario 2: Truck Routing in Customs Site
A plate recognition system will identify your truck at the entrance gate. Information will automatically be compared with relevant databases and a decision will be made regarding the need for x-ray inspection.
From this point on, the application will drive the vehicle and you will only have to intervene if something unexpected occurs.

## Slide 18: Scenario 2: Truck Routing in Customs Site
If an inspection is necessary, the truck will drive itself to defined inspection points, including x-ray, following instructions from a centralized control system that manages the operations of the border facility.
After the inspection, if everything is ok, you will be able to go back to the truck and follow your way.

## Slide 19: Current 5G-CCAM GAPs from OEM Perspective

## Slide 20: Current 5G-CCAM GAPs from OEM Perspective
When we will see common 5G deployment around EU highways?
How will be revenue stream for 5G-CCAM services?
How to act if autonomy regulations are different between neighbour countries?
How to act if GDPRs are different between neighbour countries?
Cybersecurity concerns…

## Slide 21
Thank you
Questions?

## Slide 22
Thank you
BACK-UP

## Slide 23: Message Flow – Platooning
MABX
OBU
Leader Vehicle
vEPC
Base Station
Follower Vehicle
Create Platoon
Camera & Client
Actuators & HMI
MABX
OBU
Actuators & HMI
Cloud
SWIS App
Platooning App
Create Platoon
Create Platoon
Create Platoon
Platoon Created
Platoon Created
Platoon Created
Platoon Created
Search and Join Platoon
Search and Join Platoon
Join Platoon
Join Platoon
Join Request
Join Request
Join Request
Join Accepted
Join Accepted
Join Accepted
Follower Platoon ID Saved
Platoon ID Saved
Confirmation Message
Confirmation Message

## Slide 24: Message Flow – See What I See
Jetson TX2
Follower Vehicle
LEVIS-Server
Cloud
Receive frames from port xxxx and stream over RTSP on port yyyy
Sending encoded frames over UDP
OBU
Leader Vehicle
Camera
Send raw stream
H264/H265 Encoding
Sending encoded frames over UDP
AGX Xavier
Establish RTSP session once the stream is available
Push the stream over UDP
Start live stream
Forward the request to the server
Request the live stream
Forward the request
Start RTSP server
Ok response
Start video player and try to connect to the server
H264/H265 decoding
Waiting for the stream to be available
OBU
Request a live stream
Ok response
Display
Forward the stream to the Jetson TX2
Send to display